G4Stork Description

starting from g4stork.cc

1. g4stork checks that there is an input file
2. Then g4stork reads in the input file into a StorkParseInput object
  1. The code looks for keywords in the file and uses them to set variables that define the simulation, ie what geometry to use, how many neutrons, etc
3. Then g4stork creates a logfile to store run information for the user, keff, run duration, etc
4. Then g4stork creates the random number generator
  1. The generator is used for:
    1. Setting the kinetic properties of the neutrons
    2. Doppler broadening the cross-sections
    3. Determining which interaction is chosen
    4. Determining which neutrons are duplicated or filtered out between runs
5. Then the RunManager is created
  1. this class is responsible for taking in all of the user inialized information (such as the geometry and the physics list), running the simulation, recording the results and updating the user inialized information as necessary
6. Then g4stork initializes the user defined: geometry, physics list, neutron generator, the run action, and the event action and passes them to the run manager
7. Then g4stork initializes the user defined physics and sets it in the run manager
8. Then g4stork tells the runmanager to constructs the geometry and the physics list
9. Then g4stork runs the simulation using the runmanager's BeamOn(#OfEvents) functions
10. Then g4stork outputs the results of the simulation
11. Then the program ends